## TOPCHEM®                                                    PASSIVATING  SOLUTION  PPAS

Date of issue: 2008-04-22

Revision date:

MATERIAL SAFETY DATA SHEET

1. IDENTIFICATION OF PREPARATION AND COMPANY

Product name: PŁYN PASYWACYJNY PPAS 25%

Application and use: Passivating agent for stainless steel.

Destined for professional use.

Manufacturer: Zakład Chemii Technicznej TOPCHEM

25-756 Kielce, ul. Barytowa 12, Poland

Telephone/fax: +48 41 3454747

Mobile phone 0048 601 43 91 04

2. HAZARDS IDENTIFICATION

Health hazard: Causes severe burns. Irritating to respiratory tract.

Environmental effects: Danger for environment. Pickling paste will strongly reduce pH in water.

Physical and chemical risks: When heated nitrous gases can be developed.

Fire hazard: uninflammable agent

3. COMPOSITION/INFORMATION ON INGREDIENTS

Hazardous component:

Nitric acid;   HNO3                 content            20 - 30 weight%

CAS No		7697-37-2

EEC No.		231-714-2

Classification		C	R: 35, R8

4. FIRST AID MEASURES

Measures to be taken immediately after the following ways of contact with pickling acids:

Inhalation: Supply fresh air or oxygen. Rinse nose and mouth with water. Seek medical

care even if only small troubles occur.

Ingestion: Drink at once, preferably milk or water. Thereafter 10-15 lime tablets

dissolved in water. Do not cause vomiting. Seek medical care.

Skin contact: Immediately remove any clothing soiled by agent. Rinse immediately with plenty of water, then treat with 2.5% Calcium Gluconate gel.

Next seek medical help. Do not rub with tampon.

Eye contact:  Rinse immediately with plenty of water for at least 15minutes. Thereafter seek immediate medical care (eye specialist).

Information for medical care: Inform the doctor	that the injury has been caused by contact with	hydrofluoric and nitric acid solutions. Anti-dote treatment after contact with hydrofluoric acid is HEXAFLUORINE®.

5. FIRE FIGHTING MEASURES

Danger of fire/explosion: Paste is non-flammable. In contact with metals hydrogen gas is formed in small quantities, which together with air can cause explosion. Bottles close to fire should be removed or cooled with water.

Extinguishing media: CO2, extinguishing powder or water spray. Released product should be neutralized with caustic soda.

The pickling paste will emit toxic fumes and nitrous gases in the presence of heat/fire.

## TOPCHEM®                                                    PASSIVATING  SOLUTION  PPAS

Protective clothing for firemen: Normal protective clothing.

Breathing protection: Gas mask with filter of chlorine type B (grey) and dust filter P2, according to CEN (Central European Norms).

How to clean or destroy soiled fire equipment: Thoroughly wash with water.

6. ACCIDENTAL RELEASE MEASURES

Personal precautions: Avoid direct contact. Wear eye-protection, skin-protection, rubber gloves and breathing apparatus. Keep good ventilation

Environmental precautions (water, air, soil): Prevent spillage from entering sewage or public waters.

Methods for cleaning up: Neutralize with Neutralizing Paste PN-1 or a strong alkaline compound i.e. slaked lime. Embank with sand. Arrange for pick up. Rinse with plenty of water.

Spillage and decontamination: Spillage should be picked up and disposed.

7.HANDLING AND STORAGE

Handling

Technical measures: Working place and methods should be worked out in order to avoid

direct contact. Keep good ventilation. A closed rinse water system with filtration and reuse

of clear water is recommended.

Precautions: Avoid fume generation and accumulation by using in a well-ventilated area.

Use in areas having local exhaust and general ventilation. Possibilities to rinse the eyes

with water must be available at the working place.

Storage

Technical measures: Storage room should be kept separate, cool, dry and closed to

unauthorized persons.

Storage conditions: Keep containers securely closed when not in use and in an upright

position. Store in areas where temperature remains between 0-30oC at all times.

Packaging materials: Packaging material must be of acid resistant plastic material.

Shelf life: At least 2 years in unopened bottle correctly stored.

8. EXPOSURE CONTROLS/PERSONAL PROTECTION

Ventilation System: 
           Local exhaust ventilation is recommended.

Exposure limits: 					Nitric acid

Limiting values:

PEL 			 			2ppm, 5mg/m3

REL	Short-term value -   			4ppm, 10mg/m3

Long-term value -    	                        2ppm, 5mg/m3

TLV   Short-term value -   		            4ppm, 10mg/m3

Long-term value -                   	2ppm, 5,2mg/m3

Personal protective equipment

Respiratory protection: Gas mask with a filter of the chlorine type B (grey) and dust   filter P2

Hand protection: Acid resistant rubber-gloves (neoprene gloves).

Eye protection: Face shield.

Skin and body protection: Rubber boots and acid resistant clothes, which covers all

## TOPCHEM®                                                    PASSIVATING  SOLUTION  PPAS

body parts exposed to splashes.

Specific hygienic measures: Do not inhale fumes, avoid contact with eyes, skin and clothes. It is not allowed to eat, drink and smoke at workplace. Remove contaminated clothes immediately. Wash hands and face thoroughly after working with passivating solution. Local exhaust ventilation is generally preferred because it can control the emissions of the contaminant at its source, preventing dispersion of it into the general work area.

9. PHYSICAL AND CHEMICAL PROPERTIES

Physical state (form, colour, smell) at 20oC:

Colourless gel with a minor pungent smell.

Flash point / Explosion properties: Not applicable

Vapour  pressure at 20oC:  20 hPa

pH: < 1  at 20oC

Density: ~1.2 g/cm3 at 20oC

Solubility in water:  soluble

Oxidizing properties: yes

10. STABILITY AND REACTIVITY

Stability: Stable under normal conditions, polymerization will not occur.

Conditions to avoid: Avoid high temperatures, must not be exposed to direct sunshine. When heated nitrous gases will be developed.

Material to avoid: Alkaline compounds and  will give an exothermal reaction, with heat development.

11. TOXICOLOGICAL INFORMATION

Effects on the skin: Gives corrosive damages with yellowish discoloration of the skin,

blisters and slow-healing wounds.

Effects on the eyes: Causes intensive pain and corrosive damages. Risk of irreparable damage to the eyes.

After ingestion: Gives corrosive damages with burning pain, possibly severe general effect and damage to kidneys and liver.

Upon inhalation: Inhalation of fumes or mist might cause aches, cough and difficulty in breathing. Risk for edema on the lungs.

Acute toxicity				Nitric acid

LC50 inhalative				4h, rat; 67mg/l

LD50 oral					LDL0   430mg/kg; human

12. ECOLOGICAL INFORMATION

Mobility: Do not allow passivating solution to reach ground-water  or sewage system 	 without pre-treatment.

Persistence/degradability: Will be protolysed in water to H+, NO3.

Bioaccumulation: The product is not regarded as bioaccumulative.

13. DISPOSAL CONSIDERATIONS

Methods of disposal

Waste of residual origin: Contaminated residues i.e. wastewater must be neutralized to correct its pH-value to pH 6-11.

Neutralize with  Neutralizing paste PN-1 or slaked lime.

## TOPCHEM®                                                    PASSIVATING  SOLUTION  PPAS

Contaminated packing: Rinse with plenty of water.

Additional information: A filtration system for rinse water is recommended. Effluent

must be separated and disposed of as acidic waste. It is recommended to neutralize effluent with neutralizing paste PN-1. Empty jars neutralized with PN-1 are not dangerous to environment.

14. TRANSPORT INFORMATION

Classification: UN 2031		ADR 8-2,8(b)

International regulations

Proper shipping name: Corrosive liquid, ( nitric acid)

Packaging group: II

ADR/RID (road, rail): Class 8, II

IATA/DGR (air): Class 8 - 2922

Additional information: The product is to be transported according to dangerous goods

regulations.

15. REGULATORY INFORMATION

Warning symbol:		C,

Corrosive

Hazard and safety information:

Danger phrases: (R)

R 36/38: Corrosive in contact with skin and eye.

R 35: Causes severe burns.

Sentences about safety measures

S 1/2: Keep locked up and out of the reach of children.

S 7/47: Keep container tightly closed and at temperature not exceeding 45oC.

S 23: Do not breathe fumes.

S 26: In case of contact with eyes rinse immediately with plenty of water and seek

medical advice.

S 28: After contact with skin, wash immediately with plenty of water or use

neutralizing paste PN-1.

S 36/37/39: Wear suitable protective clothing, gloves and eye/face protection.

S 42: While spraying apply protection of respiratory tract.

S 61: Avoid release to environment. Refer to special instructions/safety data sheet.

POLISH REGULATORY INFORMATION

- Ustawa z dnia 11 stycznia 2001r o substancjach i preparatach chemicznych (Dz.U. 01.11.84 z późniejszymi zmianami)

## TOPCHEM®                                                    PASSIVATING  SOLUTION  PPAS

- Rozporządzenie (WE) Nr 1907/2006 Parlamentu Europejskiego i Rady z dnia 18 grudnia  2006r w sprawie rejestracji, oceny, udzielania zezwoleń i stosowanych ograniczeń w zakresie chemikaliów (REACH) i utworzenia Europejskiej Agencji Chemikaliów (Dz.Urz.UE seria L Nr 396 z dnia 30 grudnia 2006r oraz sprostowanie Dz.Urz.UE seria L Nr 136 z dnia 29 maja 2007r)

- Rozporządzenie Min. Zdrowia z dnia 28 września 2005r w sprawie wykazu substancji

niebezpiecznych wraz z ich klasyfikacją i oznakowaniem ( Dz.U.05. 201.1674 z późn. zm.)

- Rozporządzenie Min. Zdrowia z dnia 2 września 2003r w sprawie kryteriów i sposobu

klasyfikacji substancji i preparatów chemicznych, ( Dz.U.03.171.1666 z późn. zm. )

- Rozporządzenie Min. Zdrowia  z dnia 13 listopada 2007r w sprawie karty

charakterystyki (Dz.U.07.215.1588 z późn. zm.)

- Rozporządzenie Min. Zdrowia z dnia 14 sierpnia 2002r  w sprawie obowiązku

dostarczenia karty  charakterystyki preparatów niezaklasyfikowanych jako niebezpieczne (Dz.U.02.142.1194 z późn. zm.).

- Rozporządzenie Min. Zdrowia z dnia 2 września 2003r  w sprawie oznakowania opakowań substancji niebezpiecznych i preparatów niebezpiecznych                             (Dz.U.03.173.1679 z późn. zm.)

8.   Ustawa z dnia 27 kwietnia 2001r o odpadach (Dz.U.01.62.628 z późn. zm.)

9.   Rozporządzenie Min. Środowiska z dnia 27 września 2001r w sprawie katalogu

odpadów (Dz.U.01.112.1206 z późn. zm.)

10.   Ustawa z dnia 11 maja 2001r o opakowaniach i odpadach opakowaniowych

(Dz.U.01.63.638 z późn. zm.

11.   Rozporządzenie Min. Gospodarki i Pracy z dnia 5 lipca 2004r w sprawie ograniczeń ,

zakazów lub warunków produkcji, obrotu lub stosowania substancji niebezpiecznych i

preparatów niebezpiecznych oraz zawierających je produktów(Dz.U.04.168.1762 z

późn. zm.)

12.   Rozporządzenie Min. Zdrowia z dnia 20 kwietnia 2005r w sprawie badań i pomiarów

czynników szkodliwych dla zdrowia w środowisku pracy (Dz.U.05.73.645 z późn.

zm.)

13.   Rozporządzenie Min. Zdrowia z dnia 30 grudnia 2004r w sprawie bezpieczeństwa i

higieny pracy związanej z występowaniem w miejscu pracy czynników chemicznych

(Dz.U.05.11.86 z późn. zm.)

14.   Rozporządzenie Min. Pracy i Polityki Społecznej z dnia 29 listopada 2002r w sprawie

najwyższych dopuszczalnych stężeń i natężeń czynników szkodliwych dla zdrowia w

środowisku pracy (Dz.U.02.217.1833 z późń. zm.)

15.   Rozporządzenie Min. Zdrowia z dnia 14 marca 2003r w sprawie sposobu oznakowania

miejsc, rurociągów oraz pojemników i zbiorników służących do przechowywania lub

zawierających substancje niebezpieczne lub preparaty niebezpieczne (Dz.U.03.61.552

z późn. zm.)

16.  Umowa europejska dotycząca międzynarodowego przewozu drogowego towarów

niebezpiecznych (ADR) (Dz.U.05.178.1481 z późn. zm.)

17.   Ustawa z dnia 28 października 2002r o przewozie drogowym towarów

niebezpiecznych (Dz.U.02.199.1671 z późn. zm.)

TOPCHEM®                                                   PASSIVATING  SOLUTION  PPAS

18.   Regulamin międzynarodowego przewozu kolejami towarów niebezpiecznych (RID)

wydany na podstawie Konwencji o międzynarodowym przewozie kolejami (COTIF)

sporządzony w Bernie dnia 9 maja 1980r (Dz.U.85.34.158 z późn. zm.)

19.   Rozporządzenie Min. Środowiska z dnia 24 lipca 2006r. w sprawie warunków, jakie

należy spełnić przy wprowadzeniu ścieków do wód lub ziemi oraz w sprawie substan-

cji szczególnie szkodliwych dla środowiska wodnego (Dz.U.06.137.984 z późn. zm.)

16. OTHER INFORMATION

This MSDS has been prepared according to current knowledge and based on the MSDS

of the ingredients and internet basis.